## Slide 1: Scoring the DNS Root Server System
Geoff Huston APNIC

## Slide 2: The KSK Roll
The current KSK roll at the root of the DNS includes three periods when the signed response to a query for the DNSKEY RR will exceed 1280 octets
ICANN KSK Roll presentation – 17 March 2017

## Slide 3: Root Zone Response Sizes
Response Size
% of total Responses
No responses
. Any?
. Any? queries
Trunc to ~1,440 octets
Root Servers do not normally pass back large responses

## Slide 4: Root Zone Response Sizes
Response Size
% of total Responses
99.994% of responses <= 1232 octets

## Slide 5: Root Zone “large” responses
“Large” responses from root servers are currently very uncommon (and they are probably not critical to a resolver’s operation)
The KSK roll will exercise this aspect of DNS behaviour in order to revoke the old KSK
Two questions:
  What is an ’ideal’ way for a server to pass back a large response?
  How do root servers pass back large DNS responses today?

## Slide 6: “Ideal” Large Packet Response Behaviours

## Slide 7: IPv4 and UDP
The defacto MTU for the IPv4 Internet is 1,500 octets
Larger responses in UDP typically require IP fragmentation
Firewalls don’t like fragments
  Some discard all trailing frags
  Some reassemble the packet and make an admission decision based on the re-assembled packet and then refragment the payload
UDP should not fragment the payload until the payload size reaches 1,472 octets
At this point for the DNS it’s a design trade-off between potential loss of trailing fragments or deliberately pushing the client to TCP by truncating the DNS response

## Slide 8: IPv4 and TCP
Another approach is to truncate the response at a maximum DNS payload of 1472 octets to avoid IP fragmentation, so that the resolver will re-query over TCP
BUT not every DNS resolver supports TCP
  Some 17% of resolvers, serving some 6% of end users, do not perform a TCP query following a truncated UDP response *
TCP MSS should be initially offered as the interface size, less the header overheads of IP (20 octets) and TCP (20 octets)
    1,460 is a good MSS value to offer when using IPv4
* “A Question of Protocol” http://www.potaroo.net/ispcol/2013-09/dnstcp.html

## Slide 9: Robust IPv4 Behaviour
Deliver a IPv4 UDP payload up to 1,472 octets without fragmentation at source
Do not truncate IPv4 UDP packets with a payload up to 1,472 octets *
Offer a IPv4 TCP MSS of 1,460 octets
* Assuming that the offered EDNS(0) UDP buffer size permits this

## Slide 10: IPv6 and UDP
There is no clear MTU for all IPv6
  6to4 uses 1,480 octets
  Teredo uses 1,472 octets
  “native IPv6” uses 1,500 octets
  The minimum assured unfragmented IPv6 packet size is 1,280 octets, so many systems interpret that as a “safe” MTU for IPv6

## Slide 11: IPv6 and Path MSS
IPv6 does not permit routers to fragment packets
It is possible for a sender to generate a packet that is too big for the path
When a router cannot forward a packet because it is too large for the next hop, it generate an ICMPv6 Packet Too Big diagnostic message that is sent back to the source
  The source can only “correct” the problem if it receives this ICMPv6 packet

## Slide 12: The IPv6 Problem Space
Some Firewall configurations drop trailing fragments
Some Firewall configurations drop all ICMPv6 packets
In an anycast situation some path elements may see a different anycast instance – i.e. an ICMPv6 PTB sent to the “source” may not get to the right source
Fragments require Extension Headers and many switching elements in the network drop IPv6 packets will Extension Headers
Many resolvers cannot query using TCP – either the resolvers are not configured to do so, or local firewall filter rules block TCP port 53 packets

## Slide 13: IPv6 and ICMPv6 PTB
What should the server do when it receives an ICMPv6 PTB message?
  In TCP:
    the sender can (should?) adjust its MSS to avoid sending fragments within ths session
    It should retransmit the TCP segment
    It should cache the new value and use this as the new MSS in any following TCP sessions with this resolver
  In UDP:
    It’s unclear what it should do in the case of UDP
    A conservative approach would be to push the new MSS into a forwarding table, and hold it in this cache for some system-defined time
      this system response needs to be carefully managed as uncontrolled expansion of the forwarding table with host entries represents a host vulnerability
    An alternative approach would be to ignore the PTB and rely on the client to adjust its queries via the EDNS(0) Buffer Size to elicit a truncated response from the server – but this would only be applicable to the DNS

## Slide 14: IPv6 and UDP
Despite the 1,280 assumption, it’s probably “safer” these days to use a 1500 MTU size for UDP
  The problems here with UDP fragmentation are the loss of IPv6 packets that have the Fragmentation Extension Header
    We observed an increase from 1% to 30% IPv6 packet drop rate when passing a 1,400 octet response when we dropped the server’s MTU from 1,500 to 1,280*
  Also there is the firewall filter issue and the loss of trailing fragments
  ICMPv6 PTB messages are often filtered or lost
  The use of a per-host MTU table is a potential vulnerability
  What does a front end IPv6 UDP traffic balancer do with an incoming ICMPv6 PTB message and a farm of back-end UDP engines?
The tradeoff is again between fragmented UDP loss rate and the issues with pushing the client to use TCP
* http://www.potaroo.net/ispcol/2016-10/dnsipv6.html

## Slide 15: IPv6 and TCP
Again, not every resolver supports TCP
There are path MTU issues with TCP in some instances, and the issues of ICMPv6 PTB message filtering and TCP “black holes”
A highly conservative IPv6 TCP MSS would be 1,220 octets
  This will minimize the risk of Path MTU ‘blackholing’ and fragmentation loss
  As DNS is not a very high volume application, the marginally lower carriage efficiency of a low MSS is offset by the higher probability of TCP robustness

## Slide 16: About Truncation
If a client offers a EDNS(0) UDP Buffer size, should the server honor it?
    For example:
    If the client offers a 4,096 UDP buffer size, and the response is 2,500 octets in size, is it more robust for the server to send UDP fragments of the 2,500 octet response, or just truncate immediately?
    The larger UDP response is in some sense more “correct”, assuming the honest intentions of all query agents
    Sending large DNS responses over UDP is a risk for DDOS reflection attacks

## Slide 17: Robust IPv6 Behaviour
Deliver a IPv6 UDP payload up to 1,452 octets without fragmentation and without truncation *
Do not truncate IPv6 UDP packets with a payload up to 1,452 octets *
Respond to IPv6 ICMP PTB messages with a smaller packet size consistent with the MTU in the PTB message in UDP and TCP
Offer a IPv6 TCP MSS of 1,220 octets
* Assuming that the offered EDNS(0) UDP buffer size permits this

## Slide 18: Testing Root Servers
Construct a conventional query that generates a large response
  We use a query for a DS record of a large non-existent name, using EDNS(0) with DNSSEC OK and a UDP EDNS(0) buffer size of 4096 octets
  The DNS response is 1,268 octets in size
    1296 octet IPv4 packet
    1316 octet IPv6 packet

## Slide 19: Query Tests
Query using UDP in IPv4, and respond to a truncated response by re-querying with TCP
Query using TCP in IPv4 using a local MSS of 1,460 octets
Query using UDP in IPv6, and respond to a truncated response by re-querying with TCP
Query using TCP in IPv6 using a local MSS of 1,440 octets

## Slide 20: Let’s add another test
dig . ANY @root
The response is normally 2,587 octets
Except:
  If you ask E, H or K over UDP (2,015 octet response)
  Or if you ask some instances of F (2,615 octet response)
  Or instances of F served by Cloudflare, where the response is NOTIMPL *
  Or L, where if you use V6 the response is 2,605 octets, and it’s 2,105 octets using UDP on V4 and 2,587 octets using TCP on V4
* As seen in April 2017

## Slide 21: IPv6 UDP ICMPv6 PTB test
Set up a steady sequence of queries to each root server at 10 second intervals
Synthesize ICMPv6 PTB messages in response to received UDP responses greater than 1,280 octets in size
Turn these PTB messages on for 2 minutes every hour
Run the job for 5 hours

## Slide 22: IPv6 TCP ICMPv6 PTB test
Set up a raw socket for outgoing packets, and use the pcap library to capture incoming packets
Delve deep into operating system stupidities to turn off gratuitous RSTs and TCP session firewalls
Turn off totally unhelpful interface TCP segment management
Trap the large TCP response and fake an ICMP response

## Slide 23: IPv6 TCP ICMPv6 PTB test
Tester
Root Server
Syn
Syn/Ack
Ack
DNS Query (TCP)
Ack
Large Response
ICMP PTB (MTU=1280)
????

## Slide 24: Anycast
These tests were conducted from Brisbane, Canberra (A&R network), Dallas, Frankfurt and Singapore
It may be that there are differences across the entire anycast constellation for each root letter, but no material differences were observed in the tested subset
There are major discrepancies between V4 and V6 in some cases, but that’s a different story about the issues of anycast and Dual Stack!

## Slide 25: The Scoresheets
Operates in a robust manner with large responses
Poor choice in operational behaviour
Not relevant for this behaviour profile

## Slide 26: A and J
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Does not truncate IPv4 UDP packets with a payload up to 1,472 octets
Offers a IPv4 TCP MSS of 1,460 octets
Delivers a IPv6 UDP payload up to 1,452 octets without fragmentation
Truncates IPv6 UDP packets at 1,280 octets
A responds to IPv6 ICMP PTB messages, J does not
Offers a IPv6 TCP MSS of 1,440 octets
These servers always truncate IPv6 UDP responses such that the UDP response is always under 1280 octets in size. This way they avoid fragmentation and UDP PMTU issues, but may encounter TCP issues instead. They use a large IPv6 TCP MSS. A responds to TCP ICMPv6 PTB messages, while J does not

## Slide 27: B and G
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Truncates IPv4 UDP packets at 1,280 octets
Offers a IPv4 TCP MSS of 1,460 octets
Delivers a IPv6 UDP payload up to 1,452 octets without fragmentation
Truncates IPv6 UDP packets at 1,280 octets
Responds to IPv6 ICMP PTB messages
Offers a IPv6 TCP MSS of 1,440 octets (1,220 would be more robust)
These servers always truncate IPv4 and IPv6 UDP responses such that the UDP response is always under 1280 octets in size. This way they avoid fragmentation and UDP PMTU issues, but may encounter TCP issues instead. They use a large IPv6 TCP MSS and do not respond to ICMPv6 PTB messages in TCP

## Slide 28: C, D, E, I and L
28
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Does not truncate IPv4 UDP packets with a payload up to 1,472 octets
Offers a IPv4 TCP MSS of 1,460 octets
Delivers a IPv6 UDP packet > 1,280 in size without fragmentation
Does not truncate IPv6 UDP packets with a payload up to 1,452 octets
Respond to UDP ICMPv6 PTB. D and I respond to TCP ICMPv6 PTB
Offers a IPv6 TCP MSS of 1,440 octets (1,220 would be more robust)
These servers appear to operate with a 1,500 octet MTU for both protocols in both UDP and TCP. They react to ICMPv6 PTB by clamping a 1,280 octet MTU against a host route for 10 minutes. They use a large IPv6 TCP MSS.

## Slide 29: F
29
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Does not truncate IPv4 UDP packets with a payload up to 1,472 octets
Offers a IPv4 TCP MSS of 1,460 octets
Fragments IPv6 UDP packets at 1,280 octets
Does not truncate IPv6 UDP packets with a size > 1,280
Responds to IPv6 ICMP PTB messages
Cloudflare instances offer TCP MSS of 1,220 octets, yet pass 1,271 octet segments (?)
F instances offer a TCP MSS of 1,440 octets, but fragment at 1,232 octet TCP segments
These servers appear to operate with a 1,500 octet MTU for IPv4 in both UDP and TCP. They appear to use a local 1,280 octet MTU setting for UDP in IPv6, fragmenting the outbound packet to fit within this MTU. There are subtle differences between ‘original’ F root instances and those operated by Cloudflare

## Slide 30: M
30
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Does not truncate IPv4 UDP packets with a payload up to 1,472 octets
Offers a IPv4 TCP MSS of 1,460 octets
Fragments IPv6 UDP packets at 1,280 octets
Does not truncate IPv6 UDP packets with a size > 1,280
Responds to IPv6 ICMP PTB messages
Offers a IPv6 TCP MSS of 1,440 octets, yet fragments its TCP response at 1,220 octets
These servers appear to operate with a 1,500 octet MTU for IPv4 in both UDP and TCP. They appear to use a local 1,280 octet MTU setting for UDP in IPv6, fragmenting the outbound packet to fit within this MTU. They use a large IPv6 TCP MSS.

## Slide 31: H and K
Delivers a IPv4 UDP payload up to 1,472 octets without fragmentation
Does not truncate IPv4 UDP packets with a payload up to 1,472 octets
Offers a IPv4 TCP MSS of 1,460 octets
Delivers a IPv6 UDP payload up to 1,452 octets without fragmentation
Does not truncate IPv6 UDP packets with a payload up to 1,452 octets
H responds to TCP ICMPv6 PTB, but not UDP. K does not respond in UDP
H offers a IPv6 TCP MSS of 1,440 octets. K offers 1,220
These servers appear to operate with a 1,500 octet MTU for both protocols in both UDP and TCP. They do not react to ICMPv6 PTB messages. H uses a large IPv6 TCP MSS

## Slide 32: Results

## Slide 33: Results
These three servers cannot provide a large response in IPv6 over a constrained path

## Slide 34: The Star Table

## Slide 35: Engineering Trade-Offs
There is no single “correct” way to handle large DNS responses
Each root server has made its own design decision about truncation vs fragmentation in IPv6 for large responses
As long as there is a dual stack DNS, and as long as this variation in behaviour still exists, then a persistent dual stack resolver will get the answer they are seeking from one of the DNS root servers (eventually!)
  Assuming, of course, that they are able to pose queries using both UDP and TCP, and in IPv4 and IPv6

## Slide 36: Back to the KSK roll
The 1,414 / 1,425 octet response might require a resolver to try harder, using both IPv6 and IPv4 and a number of root server letters to get the root zone’s DNSKEY RR
  If resolver cannot query over TCP/IPv4 then B and G cannot provide a complete response in UDP/IPv4
  If resolver cannot query over TCP/IPv6 then A, B, G and J cannot provide a complete response in UDP/IPv6
  If the resolver sits behind an MTU-constrained IPv6 Path, then B, C, E, G, J and L will not respond to an ICMPv6 PTB message in TCP/IPv6
  If the resolver sits behind a firewall that strips IPv6 Fragmented packets, then F and M will be unable to deliver a response in TCP/IPv6

## Slide 37: Conclusion
The various root server behaviours are to some extent anomalous, but probably not fatal to DNSSEC-validating resolvers
As long as a DNSSEC-validating resolver is persistent, and is able to try a combination of protocols and Root Servers, then it will probably be able to retrieve the larger Root Zone DNSKEY RR

## Slide 38: Questions?